Embedding it better...
µTasker Document
i.MX RT 1064 – the µTasker way

Table of Contents

# Introduction

See i.MX RT 1021 document – only changes are here
The MIMXRT1064-EVK is used as test vehicle throughout the document but any board using the part can be easily configured based on the contained details.

# Clocking

## ARM Core Clock

The ARM core is clocked by an internal clock signal called AHB_CLK_ROOT, which can be up to 600MHz.

Fraction	System PLL (528MHz PLL2) ((528MHz * 18) / fraction)	USB1 PLL (480MHz PLL3) ((480MHz * 18) / fraction)
12	792MHz	720MHz - default PFD0
13	731.0769231MHz	664.6153846MHz - default PFD1
14	678.8571429MHz	617.1428571MHz
15	633.6MHz	576MHz
16	594MHz - default PFD1 and PDF3	540MHz
17	559.0588235MHz	508.2352941MHz - default PFD2
18	528MHz	480MHz
19	500.2105263MHz	454.7368421MHz - default PFD3
20	475.2MHz	432MHz
21	452.5714285MHz	411.4285714MHz
22	432MHz	392.7272727MHz
23	413.2173913MHz	375.6521739MHz
24	396MHz - default PFD2	360MHz
25	380.16MHz	345.6MHz
26	365.5384615MHz	332.3076923MHz
27	352MHz - default PFD0	320MHz
28	339.4285714MHz	308.5714286MHz
29	327.7241379MHz	297.9310345MHz
30	316.8MHz	288MHz
31	306.58064524MHz	278.7096774MHz
32	297MHz	270MHz
33	288MHz	261.8181818MHz
34	279.5294118MHz	254.1176471MHz
35	271.5428571MHz	246.8571429MHz

The i.MX RT 1064 clock selection possibilities differs to that of the i.MX RT 1021 in the fact that it doesn't support PLL6 (500MHz Ethernet PLL) to be selected as source and instead has the ability to select PLL1, or ARM_PLL (not available in the i.MX RT 1021) instead. PLL1 is a programmable integer frequency multiplier capable of output frequencies from 650MHz up to 1.3GHz, with 864MHz default, which can be divided by 1..8 (divide by 2 – for 432MHz - is set out of reset).
The complete set of frequencies possible are shown in the following table:

Multiplier	ARM PLL PLL1) ((24MHz / multiplier) / 2)	Multiplier	ARM PLL PLL1) ((24MHz / multiplier) / 2)
54	648MHz	82	984MHz
55	660MHz	83	996MHz
56	672MHz	84	1008MHz
57	684MHz	85	1020MHz
58	696MHz	86	1032MHz
59	708MHz	87	1044MHz
60	720MHz	88	1056MHz
61	732MHz	89	1068MHz
62	744MHz	90	1080MHz
63	756MHz	91	1092MHz
64	768MHz	92	1104MHz
65	780MHz	93	1116MHz
66	792MHz	94	1128MHz
67	804MHz	95	1140MHz
68	816MHz	96	1152MHz
69	828MHz	97	1164MHz
70	840MHz	98	1176MHz
71	852MHz	99	1188MHz
72	864MHz	100	1200MHz
73	876MHz	101	1212MHz
74	888MHz	102	1224MHz
75	900MHz	103	1236MHz
76	912MHz	104	1248MHz
77	924MHz	105	1260MHz
78	936MHz	106	1272MHz
79	948MHz	107	1284MHz
80	960MHz	108	1296MHz
81	972MHz

#define PERIPH_CLK_SOURCE_ARM_PLL

AHB_CLK_ROOT

/1
/1../8
#define PERIPH_CLK_SOURCE_ARM_PLL
#define ARM_PLL_MULTIPLIER 100 // 54..108
#define PERIPH_CLK_SOURCE_ARM_PLL_DIVIDE 2 // 1..8
#define AHB_CLK_ROOT_DIVIDE 1 // 1..8
OSC_CLK

CCM_CBCMR
[PRE_PERIPH_CLK_SEL = 0x3]

CCM_CBCDR
[PERIPH_CLK_SEL = 0x0]

CCM_CBCDR
[AHB_PODF = 0x0]

PERIPH CLK
600MHz

OSC_CLK
PLL1
1.2GHz

ARM PLL

PLL2

System PLL

/2
/1../8

CCM_CACRR
[ARM_PODF = 0x1]
PRE PERIPH CLK
600MHz

CCM_ANALOG_PLL_ARM
[DIV_SELECT = 0x64]

Furthermore the PLL2 fractional divider outputs that can be used are different.

The choice of the core clock represents the major work of setting up the clocks. The following details are then specific to peripherals used in the system. Peripherals of no interest don't need to be specifically configured since they will use defaults and be gated off by the the control code.
## IPG Clock – used by ADC and XBAR

## PERCLK – used by PIT and GPT

## UART_CLK_ROOT – used by all LPUARTs

## USDHC1_CLK_ROOT/USDHC2_CLK_ROOT

## SEMC_CLK_ROOT

## FLEXSPI_CLK_ROOT

The default source of the FLEXSPI_CLK_ROOT is from the SEMC_CLK_ROOT (see previous section) with a pre-scaler of 2. As discussed in the previous section, the SEMC_CLK_ROOT is per default the PERIPH CLK (the clock root supplying the core clock pre-scaler) divided by 3. FLEXSPI_CLK_ROOT frequency must not exceed 322MHz.

SEMC_CLK_ROOT

/2
/1../8
#define FLEXSPI_CLK_FROM_SEMC_CLK
#define FLEXSPI_CLK_ROOT_DIVIDE 2 // 1..8
CCM_CSCMR1
[FLEXSPI_PODF = 0x1]

Flex
SPI

CCM_CSCMR1
[FLEXSPI_CLK_SEL = 0x0]

pll3_sw_clk

/2
/1../8
#define FLEXSPI_CLK_FROM_PLL3_SW_CLK
#define FLEXSPI_CLK_ROOT_DIVIDE 2 // 1..8
CCM_CSCMR1
[FLEXSPI_PODF = 0x1]

Flex
SPI

CCM_CSCMR1
[FLEXSPI_CLK_SEL = 0x1]

480MHz

PLL2-PFD2

/2
/1../8
#define FLEXSPI_CLK_FROM_PLL2_PFD2
#define FLEXSPI_CLK_ROOT_DIVIDE 2 // 1..8
CCM_CSCMR1
[FLEXSPI_PODF = 0x1]

Flex
SPI

CCM_CSCMR1
[FLEXSPI_CLK_SEL = 0x2]

PLL3-PFD0

/2
/1../8
#define FLEXSPI_CLK_FROM_PLL3_PFD0
#define FLEXSPI_CLK_ROOT_DIVIDE 2 // 1..8
CCM_CSCMR1
[FLEXSPI_PODF = 0x1]

FLEXSPI_CLK_ROOT
Flex
SPI

CCM_CSCMR1
[FLEXSPI_CLK_SEL = 0x3]

FlexSPI2 Clk Root
Has the last 2 options but not the first two; instead it has the options for PLL2 (528MHz) and PLL3-PD1

## LPSPI_CLK_ROOT
To add..

## TRACE_CLK_ROOT
To add..

## SAI1_CLK_ROOT/SAI2_CLK_ROOT/SAI2_CLK_ROOT
To add..

## LPI2C_CLK_ROOT – used by all LPI2C controllers

## CAN_CLK_ROOT

## SPDIF0_CLK_ROOT
To add..

## FLEXIO1_CLK_ROOT
To add..
# Internal Clock Monitoring

The i.MX RT 1064 has two peripheral outputs called CCM_CLKO1 (on GPIO_SD_B1_02, or GPIO3-22) and CCM_CLKO2 (on GPIO_SD_B1_03, or GPIO3-23) which can be attached to various interal clocks. This can be useful to verify that these clocks really have the frequencies that are expected, as well as generating signals for external usage. Fast internal signals can also be divided down by a pre-scaler with a value between 1 and 8.

These are the clocks that can be selected:

CCM_CLKO1

PLL3_SW_CLK_DIV2
PLL2_DIV2
ENET_PLL_DIV2
SEMC_CLK_ROOT
AHB_CLK_ROOT
IPG_CLK_ROOT
PERCLK_ROOT
PLL4_MAIN_CLK

CCM_CLKO2

USDHC1_CLK_ROOT
LPI2C_CLK_ROOT
OSC_CLK_ROOT
LPSPI_CLK_ROOT
USDHC2_CLK_ROOT
SAI1_CLK_ROOT
SAI2_CLK_ROOT
SAI3_CLK_ROOT
TRACE_CLK_ROOT
CAN_CLK_ROOT
FLEXSPI_CLK_ROOT
UART_CLK_ROOT
SPDIF0_CLK_ROOT

Two macros are made available to configure the pin and output the desired signals:

fnSetClock1Output(CLK, div)
fnSetClock2Output(CLK, div)

whereby examples of utilisation are:
    fnSetClock1Output(ENET_PLL_DIV2, 4);
        // output ENET_PLL/2 with pre-scaler 4 on CCM_CLKO1
    fnSetClock2Output(UART_CLK_ROOT, 1);
        // output UART_CLK_ROOT with no pre-scaler on CCM_CLKO2

# LPUART
The i.MX RT 1064 LPUART driver is shared with the Kinetis LPUART driver and supports interrupt and DMA driven modes. Minor differences due to the i.MX RT 1064 hardware are controlled by the platform definition _iMX. Sharing the driver is possible due to the high compatibility between the LPUART used in the Kinetis parts and i.MX RT 1064 and improves maintenance since only one source needs to be managed and the i.MX RT 1064 inherits the features from the mature Kinetis driver.
See the UART user's manual for general details of usage: http://www.utasker.com/docs/uTasker/uTaskerUART.PDF

It should be kept in mind that i.MX RT 1064 peripherals tend to be numbered 1..n and not 0..n-1, as is the case with Kinetis peripherals. To avoid confusion it is recommended to use the defines
iMX_LPUART_1
iMX_LPUART_2
iMX_LPUART_n

instead of channel numbers, whereby iMX_LPUART_1 is in fact 0.

The LPUARTs can be multiplexed onto various physical pins. When a specific LPUART is used it defaults to a certain set of pins if nothing else is specified – the following gives a list of the LPUART multiplex pins and the definition that can be used to control the use of alternatives where possible and if required:

Channel	Default	Alternative 1	Alternative 2
iMX_LPUART_1 (0) LPUART1_RXD LPUART1_TXD	GPIO_AD_B0_07 GPIO_AD_B0_06
iMX_LPUART_2 (1) LPUART2_RXD LPUART2_TXD	GPIO_AD_B1_09 GPIO_AD_B1_08	LPUART2_ON_EMC GPIO_EMC_23 GPIO_EMC_22
iMX_LPUART_3 (2) LPUART3_RXD LPUART3_TXD	GPIO_AD_B0_15 GPIO_AD_B0_14	LPUART3_ON_EMC GPIO_EMC_07 GPIO_EMC_06
iMX_LPUART_4 (3) LPUART4_RXD LPUART4_TXD	GPIO_AD_B1_11 GPIO_AD_B1_10	LPUART4_ON_EMC_LOW GPIO_EMC_03 GPIO_EMC_02	LPUART4_ON_EMC_HIGH GPIO_EMC_33 GPIO_EMC_32
iMX_LPUART_5 (4) LPUART5_RXD LPUART5_TXD	GPIO_AD_B0_11 GPIO_AD_B0_10	LPUART5_ON_EMC GPIO_EMC_39 GPIO_EMC_38
iMX_LPUART_6 (5) LPUART6_RXD LPUART6_TXD	GPIO_SD_B1_01 GPIO_SD_B1_00	LPUART6_ON_EMC GPIO_EMC_13 GPIO_EMC_12
iMX_LPUART_7 (6) LPUART7_RXD LPUART7_TXD	GPIO_SD_B0_05 / GPIO_SD_B0_04	LPUART7_ON_EMC GPIO_EMC_35 GPIO_EMC_34
iMX_LPUART_8 (7) LPUART8_RXD LPUART8_TXD	GPIO_SD_B1_03 GPIO_SD_B1_02	LPUART8_ON_EMC GPIO_EMC_27 GPIO_EMC_26

For example, if LPUART2 is used its default pin-out Tx/RX is on GPIO_AD_B1_08/GPIO_AD_B1_09 [GPIO1-IO24 and GPIO1-IO25]
but can be set instead to

 GPIO_EMC_22/GPIO_EMC_23 [GPIO2-IO22 and GPIO2-IO23]
by enabling the define LPUART2_ON_EMC. This define is set in app_hw_iMX.h

It is to be noted that the µTasker project is often chosen due to its immediate support for free-running UART Rx DMA on all serial interfaces, which is something that is generally not found in other solutions. The i.MX RT 1021 thus could immediately inherit this operation.
# LPI2C
The i.MX RT 1064 LPI2C driver is shared with the Kinetis LPUART driver and supports interrupt and DMA driven modes. Minor differences due to the i.MX RT 1064 hardware are controlled by the platform definition _iMX. Sharing the driver is possible due to the high compatibility between the LPI2C used in the Kinetis parts and i.MX RT 1064 and improves maintenance since only one source needs to be managed and the i.MX RT 1064 inherits the features from the mature Kinetis driver.
See the I2C user's manual for general details of usage:
http://www.utasker.com/docs/uTasker/uTasker_I2C.pdf

It should be kept in mind that i.MX RT 1064 peripherals tend to be numbered 1..n and not 0..n-1, as is the case with Kinetis peripherals. To avoid confusion it is recommended to use the defines
iMX_LPI2C_1
iMX_LPI2C_2
iMX_LPI2C_n

instead of channel numbers, whereby iMX_LPI2C_1 is in fact 0.

# FLEXCAN
The i.MX RT 1064 CAN driver is shared with the Kinetis CAN driver. Minor differences due to the i.MX RT 1064 hardware are controlled by the platform definition _iMX. Sharing the driver is possible due to the high compatibility between the FLEXCAN used in the Kinetis parts and i.MX RT 1064 and improves maintenance since only one source needs to be managed and the i.MX RT 1021 inherits the features from the mature Kinetis driver.
The FLEXCAN in the i.MX RT 1064 supports 64 receive buffers as opposed to the 16 in the FLEXCAN in the Kinetis parts.
See the CAN user's manual for general details of usage:
http://www.utasker.com/docs/uTasker/uTaskerCAN.PDF

It should be kept in mind that i.MX RT 1064 peripherals tend to be numbered 1..n and not 0..n-1, as is the case with Kinetis peripherals. To avoid confusion it is recommended to use the defines
iMX_FLEXCAN_1
iMX_FLEXCAN_2

instead of channel numbers, whereby iMX_FLEXCAN_1 is in fact 0.
# PIT

The i.MX RT 1064 PIT driver is shared with the Kinetis PIT driver. Minor differences due to the i.MX RT 1064 hardware are controlled by the platform definition _iMX. Sharing the driver is possible due to the high compatibility between the PIT used in the Kinetis parts and i.MX RT 1064 and improves maintenance since only one source needs to be managed and the i.MX RT 1064 inherits the features from the mature Kinetis driver.
See the HW timer user's manual for general details of usage: http://www.utasker.com/docs/uTasker/uTaskerHWTimers.PDF

(see TEST_PIT [TEST_PIT_SINGLE_SHOT, TEST_PIT_PERIODIC and TEST_PIT_64_BIT in ADC_Timers.h as reference to use).

# GPT

The i.MX RT 1021 has two General Purpose Timers (GPT), which are 32 bit up-counters with 12-bit pre-scaler (1..4096) clocked from PERCLK but with programmable counter clock source. Drivers are active when the project define SUPPORT_TIMER is enabled in app_hw_iMX.h.
The GPTs supports capture mode on programmable edges of their associalted timer input pins (GPT_CAPTUREx) and can generate an event on their output compare pins (GPT_COMPAREx), as well as an interrupt when the counter reaches a programmed value.
Capture mode support is active when SUPPORT_CAPTURE is enabled.
Programmable clock sources to the prescaler are:
- Crystal oscillator (with its own 1..16 prescaler)
- External GPT_CLK input
- Peripheral Clock
- Low frequency reference clock (32kHz)
- High frequency reference clock

Each GPT has two input capture channels and three output compare channels and operates either in Restart (based on compare channel 1) or Free-run mode of operation.

The GPT driver interface is highy compatible with the FlexTimer/TPM driver in the Kinetis project. Each GPT can be used to generate periodic or single shot interrupts, capture inputs or generate a square wave, low or high edge on match. See the Hardware Timer Guide at https://www.utasker.com/docs/uTasker/uTaskerHWTimers.PDF for more details.

Unfortunately, although the GPT can generate a square wave output, it can't generate PWM outputs. Also it can't trigger DMA operations.

The GPTs input/outpus can be multiplexed onto various physical pins. When a specific GPT is used it defaults to a certain set of pins if nothing else is specified – the following gives a list of the GPT multiplex pins and the definition that can be used to control the use of alternatives where possible and if required:

GPT	Default	Alternative 1	Alternative 2
iMX_GPT_1 (0) GPT1_CLK	GPIO_B1_04	GTP1_CLK_ON_AD_B0 / GPIO_AD_B0_13
iMX_GPT_2 (1) GPT2_CLK	GPIO_AD_B1_02	GTP2_CLK_ON_AD_B0 GPIO_AD_B0_09

# DMA

The i.MX RT 1064 DMA driver is shared with the Kinetis eDMA driver. Minor differences due to the i.MX RT 1064 hardware are controlled by the platform definition _iMX. Sharing the driver is possible due to the high compatibility between the eDMA and DMA MUX used in the Kinetis parts and i.MX RT 1064 and improves maintenance since only one source needs to be managed and the i.MX RT 1064 inherits the features from the mature Kinetis driver.

# GPIO

The i.MX RT 1064 GPIO / peripheral concept is quite different to the Kinetis concept. See the following video for an overview and also details concerning how the project was solved to ensure compatibility between Kinetis and i.MX RT:
https://www.youtube.com/watch?v=SmFTi8hlba0&list=PLWKlVb_MqDQFZAulrUywU30v869JBYi9Q&index=29

GPIOs can also be used as interrupts (see IRQ_TEST in Port_Interrupts.h as reference to use).

Each GPIO can be configured to generate an interrupt on low levels, high levels, falling edges or rising edges (or both falling and rising edges). The µTasker GPIO interrupt driver allows the user to assign an individual interrupt callback to each GPIO but it is useful to understand that the i.MX RT 1021 actually has the following interrupt vectors:
- PORT1-0 – individual vector for these pins
- PORT1-1
- PORT1-2
- PORT1-3
- PORT1-4
- PORT1-5
- PORT1-6
- PORT1-7

- PORT1-15..PORT1-8 – these 8 pins share a single vector

- PORT1-31..PORT1-16 – these 16 pins share a single vector

- PORT2-15..PORT2-0 – these 16 pins share a single vector
- PORT2-31..PORT2-16 – these 16 pins share a single vector
- PORT3-15..PORT3-0 – these 16 pins share a single vector
- PORT3-31..PORT3-16 – these 16 pins share a single vector
- PORT5-15..PORT5-0 – these 16 pins share a single vector
- PORT5-31..PORT5-16 – these 16 pins share a single vector

PORT1-0..PORT1-7 are the most efficient interrupts since the handler doesn't need to identify which port bits caused the interrupt before dispatching the user interrupt callback.
Ports with an interrupt vector shared by more than one pin are slightly less efficient due to the need to identify which source or sources caused the interrupt and then dispatch one or more call-backs. When multiple GPIO input interrupts are pending at the same time the callbacks are dispatched in the order of the lower pin number up to the highest pin number.
# RAM and Cache

he i.MX RT 1064 contains 1M of internal RAM, whereby 512k is fixed (OCRAM2) and 512k is configurable (FlexRAM) which is constructed of 16 banks of 32k each. These banks can each be assigned to one three areas (FlexRAM controller):
- OCRAM General RAM operates at 1/4 the core clock speed (32 bit wide). This is cacheable, meaning that if L1 cache is enabled data content that is already in cache is used to avoid needing to perform the OCRAM access.
- ITCM Instruction Tightly Coupled Memory (64 bit wide) that is optimised for instruction execution at the maximum core speed. Non-cacheable (also since already optimally fast) and so no potential cache synchronisation problems.
- DTCM Data Tightly Coupled Memory (64 bit wide) that is optimised for data access at the maximum core speed. Non-cacheable (also since already optimally fast) and so no potential cache synchronisation problems.

For full details concerning the FlexRAM and optimal configuration to match an applications memory requirements NXP has prepared the application note AN12077 which can be found at https://www.nxp.com/docs/en/application-note/AN12077.pdf

The i.MX RT 1064 has L1 cache with 32kBytes instruction cache and 32kBytes data cache. NXP has prepared the application note AN12042 which can be found at https://www.nxp.com/docs/en/application-note/AN12042.pdf
Use of the cache can ensure high speed operation even when the source of code or data is in a slower memory by avoiding to have to unnecessarily fetch the data when it has been loaded once to the cache.
When the cache is enabled it caches from OCRAM and QSPI-Flash; it neither caches ITCM nor DTCM, which are already tightly coupled to the core.
The application can decide whether it uses data or instruction cache with the defines
#define ENABLE_INSTRUCTION_CACHE
and
#define ENABLE_DATA_CACHE

The FlexRAM controller configures the RAM banks at reset based on eFuse settings. The standard setting (when nothing else has been programmed) is for 256k OCRAM, 128k DTCM and 128k ITCM; the ROM loader may use the first 64k of the OCRAM when it operates.
This default setting is assumed in the µTasker project to avoid special configuration requirements and therefore out of reset the banks are configured to give this memory map and layout:

0x00000000
0x0001ffff
0x20000000
0x2001ffff
0x20200000

0x2023ffff

32k Banks

0
1
2
3

4
5

6
7
ITC
128k
DTC
128k
OCR
256k

0123456789111111
        012345
OOOODDIIIIDDOOOO
12
13
14
15

10
11
8
9

Assuming it is decided that an application were best configured to have 11 banks for ITCM (so that the code could be completely located there – 352k) and 5 banks for data (so that up to 160k of data could be accesses at optimal speed) and no OCRAM the 16 banks could be configured as follows:

0x2023ffff
32k Banks
OCR
0k

IIIIIIIIIIIDDDDD

0x00000000
0x20000000
0x20027fff
0x20200000
0x00057fff

11
12

0
1
ITC
352k
DTC
160k
2
3
4
15
5
6
7
8
9
10
13
14

The µTasker FlexRAM driver always uses the bank order from instruction use to data use (if OCRAM were used it would be inserted between the two). The most important thing to understand is that when the bank use is modified the address range of the bank is also changed (it is moved in the memory map). This means that data that was in OCR before the change (in the default configuration) still exists in the bank memory but is now addressed in the ITC or DTC memory space instead.
This behaviour makes it complicated to change the memory configuration at run time because it means that any memory used before the change (eg. The stack or initialised variables) are usually at completely different locations after the change. Typically this will cause a program that simply changes the bank configuration without respecting the fact that its memory moves during the process to immediately fail. For this reason such changes are generally not performed during program operation; if such a configuration is changed it tends to be performed before any variable initialisation and also from code running in other sources and without stack dependency.
The µTasker concept assumes that code and variables fit in the internal RAM and so OCRAM is avoided. The division between ITC and OTC is performed at system initialisation automatically to allocate ITC banks to the code space and DTC banks to data space in such a way as to have as much DTC available as possible for heap and stack. If code of 340k were encountered it would thus assign 352k ITC and 160k DTC, as in the example. If less code were encountered additional banks would be assigned to DTC in order to maximise heap and stack availability. Code and data are automatically in the highest performance RAM areas and caching is not required to achieve optimal performance (without caching, no additional synchronisation of data is required).
There is an important reason for choosing the bank ordering: In the default configuration bank 7 is assigned to OCR but will not be used by the ROM loader (the ROM loader may use up to 64k only). After the bank swap is performed this bank is the last bank in DTM, whereby the stack pointer is located near the top, but leaving some additional space above it for 'preserved' variables. The advantage of this is that an application can always write values to the preserved area before a reset and these values will not be modified by the ROM loader. The µTasker boot loader or another application can then read these values, even if the application uses a different RAM bank configuration; as long as its stack pointer is put to near the end of the final bank it will automatically be referenced to the the preserved data area! The preserved area is used in the µTasker project for communicating between applications and the µTasker boot loaders, but can also be used by custom applications for holding data that is guaranteed to be preserved across warm resets.
Due to the nature of the memory operation of the i.MX RT 1064, its configuration requirement to achieve optimal performance and the desire to allow µTasker users to benefit from these with no additional effort the RAM bank management is an integral part of the µTasker boot strategy and the µTasker Boot Loader (see Boot Mode section) an integral part of every project (apart from when a stand-alone application is loaded in a debug environment for test purposes).

# Boot Mode

# Ethernet

# Low Power and Battery Backup

The i.MX RT 1064 supports three RU modes
- Overdrive Run
- Full Speed Run
- Low Power Run
and four low power modes:
- System IDLE
- Low Power IDLE
- SUSPEND
- SNVS
The i.MX RT 1064 has a coin cell input that can be used to supply power to parts of the device that require minimum operation and data retention when the main power is removed.
Specifically, the energy supplied by the input (VDD_SNVS_IN 2.4V..3.6V) is used to retain the state of the processors pads, supply power to its internal real time clock and retal data in its SNVS (secure non-volatile storage module) module. An internal low drop out regulator reduces the input voltage to a stable 1.1V for the internal operation and requires a 220nF capacitor on the VDD_SNVS_CAP output for stability. In addition a serier input resistor is recommended to reduce suge current when connecting the battery (ca. 1K is typically).
The register CCM_ANALOG_MISC0 contains a switch called DISCON_HIGH_SNVS which by default connects the VDD_HIGH_IN power input to the VDD_SNVS_IN input when the main supply is present, thus supplying this circuit's energy from the main power supply (and optionally charging the coin cell from the main power supply). This can to be set to '1' to move this connection
There are 128 bits of battery-backed memory in the SNVS which can be read/written as 4 long words as registers SNVS_LPGPR0, SNVS_LPGPR1, SNVS_LPGPR2 and SNVS_LPGPR3.
These registers are however reset to 0x00000000 when a tamper event is detected by the chip (in order to clear user keys stored here) and in systems not using the tamper detection circuity it is necessary to disable the clearing mechanism by setting bit 24 in SNVS_LPCR. This bit is referred to by user documentatio but is otherwise not defined by the literature. Since this control flag is also retained across software resets it is suitable for enabling general purpose storage to these registers. Read/write access do however need to be long word accesses for correction operation!.

# Conclusion

Modifications:
V0.00 23.06.2020: Initial version in development
# Appendix A – Hardware Dependencies

## Space for first Appendix